## Slide 1: Chapter 2 Force Vectors
Sections 2.1, 2.2, 2.3, 2.4

## Slide 2: QUIZ
1. Which one of the following is a scalar quantity?
A) Force B) Position C) Mass D) Velocity
2. What is the resultant of A + B if :
A = 2i -3j and B = -1i +6j
3. What is the magnitude and direction of the resultant from #2?
4. Which of these symbolizes the addition of A + B = resultant ?
Notes: Answers:
1. C
2. 1i +3j 3.16 Ɵ = -71.6 (from negative x-axis) or 108.44 from positive x-axis

## Slide 3: SCALARS AND VECTORS (Section 2.1)
Scalars Vectors
Examples: mass, volume force, velocity
Characteristics: It has a magnitude It has a magnitude
(positive or negative) and direction
Addition rule: Simple arithmetic Parallelogram law
Special Notation: None Bold font, a line, an
arrow or a “carrot”

## Slide 4: VECTOR OPERATIONS (Section 2.2)
Scalar Multiplication
and Division

## Slide 5: VECTOR ADDITION USING EITHER THE PARALLELOGRAM LAW OR TRIANGLE
Parallelogram Law:
Triangle method (always ‘tip to tail’):
How do you subtract a vector?
How can you add more than two concurrent vectors graphically ?

## Slide 6: “Resolution” of a vector is breaking up a vector into components. It is kind of like using the parallelogram law in reverse.
RESOLUTION OF A VECTOR

## Slide 7
Law of Sines

## Slide 11
Find the magnitude and angle of the resultant force.

## Slide 12
Find the magnitude and angle of the resultant force.

## Slide 13: CARTESIAN VECTOR NOTATION (Section 2.4)
Each component of the vector is shown as a magnitude and a direction.
We ‘resolve’ vectors into components using the x and y axes system.
The directions are based on the x and y axes. We use the “unit vectors” i and j to designate the x and y axes.

## Slide 14: Unit Vectors
vector
unit vector
Notes: Note subscripts; although this is an awkward way to define the “sine” of the angle (from the theta x perspective) it’s a good example of why subscripts are important.

## Slide 15
For example,
F = Fx i + Fy j
The x and y axes are always perpendicular to each other. Together,they can be directed at any inclination.

## Slide 16: ADDITION OF SEVERAL VECTORS
Step 3 is to find the magnitude and angle of the resultant vector.
Step 1 is to resolve each force into its components
Step 2 is to add all the x components together and add all the y components together. These two totals become the resultant vector.

## Slide 17: Example of this process,

## Slide 18: You can also represent a 2-D vector with a magnitude and angle.

## Slide 19: APPLICATION OF VECTOR ADDITION
There are four concurrent cable forces acting on the bracket.
How do you determine the resultant force acting on the bracket ?

## Slide 20
EXAMPLE
Given: Three concurrent forces acting on a bracket.
Find: The magnitude and angle of the resultant force.
Plan:
a) Resolve the forces in their x-y components.
b) Add the respective components to get the resultant vector.
c) Find magnitude and angle from the resultant components.

## Slide 21
EXAMPLE (continued)
F1 = { 15 sin 40° i + 15 cos 40° j } kN
= { 9.642 i + 11.49 j } kN
F2 = { -(12/13)26 i + (5/13)26 j } kN
= { -24 i + 10 j } kN
F3 = { 36 cos 30° i – 36 sin 30° j } kN
= { 31.18 i – 18 j } kN

## Slide 22
EXAMPLE (continued)
Summing up all the i and j components respectively, we get,
FR = { (9.642 – 24 + 31.18) i + (11.49 + 10 – 18) j } kN
= { 16.82 i + 3.49 j } kN
x
y

FR
FR = ((16.82)2 + (3.49)2)1/2 = 17.2 kN
 = tan-1(3.49/16.82) = 11.7°

## Slide 23
GROUP PROBLEM SOLVING
Given: Three concurrent forces acting on a bracket
Find: The magnitude and angle of the resultant force.
Plan:
a) Resolve the forces in their x-y components.
b) Add the respective components to get the resultant vector.
c) Find magnitude and angle from the resultant components.

## Slide 24
F1 = { (4/5) 850 i - (3/5) 850 j } N
= { 680 i - 510 j } N
F2 = { -625 sin(30°) i - 625 cos(30°) j } N
= { -312.5 i - 541.3 j } N
F3 = { -750 sin(45°) i + 750 cos(45°) j } N
{ -530.3 i + 530.3 j } N
GROUP PROBLEM SOLVING (continued)

## Slide 25
GROUP PROBLEM SOLVING (continued)
Summing up all the i and j components respectively, we get,
FR = { (680 – 312.5 – 530.3) i + (-510 – 541.3 + 530.3) j }N
= { - 162.8 i - 521 j } N
FR = ((162.8)2 + (521)2) ½ = 546 N
= tan–1(521/162.8) = 72.64° or
From Positive x axis  = 180 + 72.64 = 253 °

y
x
FR

## Slide 26
ATTENTION QUIZ
1. Resolve F along x and y axes and write it in vector form. F = { ___________ } N
A) 80 cos (30°) i - 80 sin (30°) j
B) 80 sin (30°) i + 80 cos (30°) j
C) 80 sin (30°) i - 80 cos (30°) j
D) 80 cos (30°) i + 80 sin (30°) j
2. Determine the magnitude of the resultant (F1 + F2) force in N when F1 = { 10 i + 20 j } N and F2 = { 20 i + 20 j } N .
A) 30 N B) 40 N C) 50 N
D) 60 N E) 70 N
30°
x
y
F = 80 N
Notes: Answers:
1. C
2. C

## Slide 27
Find the magnitude and angle of the resultant force.