## Slide 1: Chapter 4
NOT section 5
Sections 6-10

## Slide 2
READING QUIZ
1. In statics, a couple is defined as __________ separated by a perpendicular distance.
A) two forces in the same direction.
B) two forces of equal magnitude.
C) two forces of equal magnitude acting in the same direction.
D) two forces of equal magnitude acting in opposite directions.
2. Are these two equivalent loadings?
Notes: Answers:
1. D
2. yes

## Slide 3
APPLICATIONS
A torque or moment of 12 N · m is required to rotate the wheel. Which one of the two grips of the wheel above will require less force to rotate the wheel?

## Slide 4
APPLICATIONS (continued)
The crossbar lug wrench is being used to loosen a lug net. What is the effect of changing dimensions a, b, or c on the force that must be applied?

## Slide 5
MOMENT OF A COUPLE
A couple is defined as two parallel forces with the same magnitude but opposite in direction separated by a perpendicular distance d.
The moment of a couple is defined as
MO = F d (using a scalar analysis) or as
MO = r  F (using a vector analysis).
Here r is any position vector from the line of action of –F to the line of action of F.

## Slide 6
MOMENT OF A COUPLE (continued)
The net external effect of a couple is that the net force equals zero and the magnitude of the net moment equals F d
Moments due to couples can be added using the same rules as adding any vectors.
Since the moment of a couple depends only on the distance between the forces, the moment of a couple is a free vector. It can be moved anywhere on the body and have the same external effect on the body.

## Slide 7: Find the moment
What moment is produced if the force is 75 pounds?

## Slide 8: Find the moment
What moment is produced if the force is 75 pounds?

## Slide 9
EXAMPLE - SCALAR APPROACH
Given: Two couples act on the beam and d equals 8 ft.
Find: The resultant couple
Plan:
1) Resolve the forces in x and y directions so they can be treated as couples.
2) Determine the net moment due to the two couples.

## Slide 10
The x and y components of the top 60 lb force are:
(4/5)(60 lb) = 48 lb vertically up
(3/5)(60 lb) = 36 lb to the left
Similarly for the top 40 lb force:
(40 lb) (sin 30°) up
(40 lb) (cos 30°) to the left
The net moment equals to
+ M = -(48 lb)(4 ft) + (40 lb)(cos 30º)(8ft)
= -192.0 + 277.1 = 85.1 ft·lb
EXAMPLE - SCALAR APPROACH

## Slide 11
EXAMPLE – VECTOR APPROACH
Given: A force couple acting on the rod.
Find: The couple moment acting on the rod in Cartesian vector notation.
Plan:
1) Use M = r  F to find the couple moment.
2) Set r = rAB and F = {14 i – 8 j – 6 k} N .
3) Calculate the cross product to find M.
A
B

## Slide 12
rAB = {0.8 i + 1.5 j – 1 k} m
F = {14 i – 8 j – 6 k} N
M = rAB  F
= {i (-9 – (8)) – j (- 4.8 – (-14)) + k (-6.4 – 21)} N·m
= {-17 i – 9.2 j – 27.4 k} N·m
=
N·m
i
j
k
0.8 1.5 -1
14 -8 -6
A
B
EXAMPLE – VECTOR APPROACH

## Slide 13
GROUP PROBLEM SOLVING – SCALAR APPROACH
Given: Two couples act on the beam. The resultant couple is zero.
Find: The magnitudes of the forces P and F and the distance d.
PLAN:
1) Use definition of a couple to find P and F.
2) Resolve the 300 N force in x and y directions.
3) Determine the net moment.
4) Equate the net moment to zero to find d.

## Slide 14
GROUP PROBLEM SOLVING – SCALAR APPROACH
From the definition of a couple:
P = 500 N and
F = 300 N.
Resolve the 300 N force into vertical and horizontal components. The vertical component is (300 cos 30º) N and the horizontal component is (300 sin 30º) N.
Now solve this equation for d.
d = (1000 + 60 sin 30º) / (300 cos 30º) = 3.96 m
It was given that the net moment equals zero. So
+ M = - (500)(2) + (300 cos 30º)(d) - (300 sin 30º)(0.2) = 0

## Slide 15
GROUP PROBLEM SOLVING – VECTOR APPROACH
Given: F = {25 k} N and - F = {- 25 k} N
Find: The couple moment acting on the pipe assembly using Cartesian vector notation.
PLAN:
1) Use M = r  F to find the couple moment.
2) Set r = rAB and F = {25 k} N .
3) Calculate the cross product to find M.

## Slide 16
rAB = { - 350 i – 200 j } mm
= { - 0.35 i – 0.2 j } m
F = {25 k} N
=
M = rAB  F
= { i ( - 5 – 0 ) – j (- 8.75 – 0) + k (0) } N · m
= { -5 i + 8.75 j } N · m
N · m
GROUP PROBLEM SOLVING – VECTOR APPROACH

## Slide 17
1. A couple is applied to the beam as shown. Its moment equals _____ N·m.
A) 50 B) 60
C) 80 D) 100
ATTENTION QUIZ
2. You can determine the couple moment as M = r  F
If F = { -20 k} lb, then r is
A) rBC B) rAB
C) rCB D) rAC
3
4
5
1m
2m
50 N
Notes: Answers:
1. B – remember the definition of a couple, the picture shows the magnitude on one vector, the other vector shows the direction; so, if they are a couple, they have to have the same magnitude and same direction.
2. A

## Slide 18
Do you remember from reading?
1. A general system of forces and couple moments acting on a rigid body can be reduced to a ___ .
1) single force.
2) single moment.
3) single force and two moments.
4) single force and a single moment.
2. The original force and couple system and an equivalent force-couple system have the same _____ effect on a body.
1) internal 2) external
3) internal and external 4) microscopic
Notes: Answers:
1. D
2. B

## Slide 19
Equivalent Situations
What is the resultant effect on the person’s hand when the force is applied in four different ways ?

## Slide 20
APPLICATIONS (continued)
Several forces and a couple moment are acting on this vertical section of an I-beam.
Can you replace them with just one force and one couple moment at point O that will have the same external effect? If yes, how will you do that?
| |

## Slide 21
AN EQUIVALENT SYSTEM (Section 4.7)
When a number of forces and couple moments are acting on a body, it is easier to understand their overall effect on the body if they are combined into a single force and couple moment having the same external effect
The two force and couple systems are called equivalent systems since they have the same external effect on the body.
=

## Slide 22
MOVING A FORCE ON ITS LINE OF ACTION
Moving a force from A to O, when both points are on the vectors’ line of action, does not change the external effect. Hence, a force vector is called a sliding vector. (But the internal effect of the force on the body does depend on where the force is applied).

## Slide 23
MOVING A FORCE OFF OF ITS LINE OF ACTION
Moving a force from point A to O (as shown above) requires creating an additional couple moment. Since this new couple moment is a “free” vector, it can be applied at any point P on the body.

## Slide 24
RESULTANTS OF A FORCE AND COUPLE SYSTEM
(Section 4.8)
When several forces and couple moments act on a body, you can move each force and its associated couple moment to a common point O.
Then add all the forces and couple moments together and find one resultant force-couple moment pair.

## Slide 25
RESULTANT OF A FORCE AND COUPLE SYSTEM (continued)
If the force system lies in the x-y plane (the 2-D case), then the reduced equivalent system can be obtained using the following three scalar equations.

## Slide 26
FURTHER REDUCTION OF A FORCE AND COUPLE SYSTEM (Section 4.9)
If FR and MRO are perpendicular to each other, then the system can be further reduced to a single force, FR , by simply moving FR from O to P.
=
=
In three special cases, concurrent, coplanar, and parallel systems of forces, the system can always be reduced to a single force.

## Slide 27
EXAMPLE #1
Given: A 2-D force and couple system as shown.
Find: The equivalent resultant force and couple moment acting at A and then the equivalent single force location along the beam AB.
Plan:
1) Sum all the x and y components of the forces to find FRA.
2) Find and sum all the moments resulting from moving each force to A.
3) Shift the FRA to a distance d such that d = MRA/FRy

## Slide 28
EXAMPLE #1 (continued)
+  FRx = 25 + 35 sin 30° = 42.5 lb
+  FRy = 20 + 35 cos 30° = 50.31 lb
+ MRA = 35 cos30° (2) + 20(6) – 25(3)
= 105.6 lb·ft
The equivalent single force FR can be located on the beam AB at a distance d measured from A.
d = MRA/FRy = 105.6/50.31 = 2.10 ft.
FR = ( 42.52 + 50.312 )1/2 = 65.9 lb  = tan-1 ( 50.31/42.5) = 49.8 °
FR

## Slide 29
EXAMPLE #2
Given: The building slab has four columns. F1 and F2 = 0.
Find: The equivalent resultant force and couple moment at the origin O. Also find the location (x,y) of the single equivalent resultant force.
Plan:
1) Find FRO = Fi = FRzo k
2) Find MRO =  (ri  Fi) = MRxO i + MRyO j
3) The location of the single equivalent resultant force is given as x = -MRyO/FRzO and y = MRxO/FRzO
o

## Slide 30
EXAMPLE #2 (continued)
FRO = {-50 k – 20 k} = {-70 k} kN
MRO = (10 i)  (-20 k) + (4 i + 3 j)x(-50 k)
= {200 j + 200 j – 150 i} kN·m
= {-150 i + 400 j } kN·m
The location of the single equivalent resultant force is given as,
x = -MRyo/FRzo = -400/(-70) = 5.71 m
y = MRxo/FRzo = (-150)/(-70) = 2.14 m
o

## Slide 31
CONCEPT QUIZ
1. The forces on the pole can be reduced to a single force and a single moment at point ____ .
A) P B) Q C) R
D) S E) Any of these points.
2. Consider two couples acting on a body. The simplest possible equivalent system at any arbitrary point on the body will have
A) one force and one couple moment.
B) one force.
C) one couple moment.
D) two couple moments.
Notes: Answers:
E
C

## Slide 32
GROUP PROBLEM SOLVING
Given: A 2-D force and couple system as shown.
Find: The equivalent resultant force and couple moment acting at A.
Plan:
1) Sum all the x and y components of the forces to find FRA.
2) Find and sum all the moments resulting from moving each force to A and add them to the 500 lb - ft free moment to find the resultant MRA .

## Slide 33
GROUP PROBLEM SOLVING (continued)
+  Fx = (4/5) 150 lb + 50 lb sin 30° = 145 lb
+  Fy = (3/5) 150 lb + 50 lb cos 30° = 133.3 lb
Now find the magnitude and direction of the resultant.
FRA = ( 145 2 + 133.3 2 )1/2 = 197 lb and  = tan-1 ( 133.3/145) = 42.6 °
+ MRA = { (4/5)(150)(2) – 50 cos30° (3) + 50 sin30° (6) + 500 }
= 760 lb·ft
Summing the force components:

## Slide 34
GROUP PROBLEM SOLVING (continued)
Given: Handle forces F1 and F2 are applied to the electric drill.
Find: An equivalent resultant force and couple moment at point O.
Plan:
a) Find FRO =  Fi
b) Find MRO =  MC +  ( ri  Fi )
Where,
Fi are the individual forces in Cartesian vector notation (CVN).
MC are any free couple moments in CVN (none in this example).
Ri are the position vectors from the point O to any point on the line of action of Fi .

## Slide 35
SOLUTION
F1 = {6 i – 3 j – 10 k} N
F2 = {0 i + 2 j – 4 k} N
FRO = {6 i – 1 j – 14 k} N
r1 = {0.15 i + 0.3 k} m
r2 = {-0.25 j + 0.3 k} m
MRO = r1  F1 + r2  F2
= {0.9 i + 3.3 j – 0.45 k + 0.4 i + 0 j + 0 k} N·m
= {1.3 i + 3.3 j – 0.45 k} N·m
MRO = {
} N·m

## Slide 36
ATTENTION QUIZ
1. For this force system, the equivalent system at P is ___________ .
A) FRP = 40 lb (along +x-dir.) and MRP = +60 ft ·lb
B) FRP = 0 lb and MRP = +30 ft · lb
C) FRP = 30 lb (along +y-dir.) and MRP = -30 ft ·lb
D) FRP = 40 lb (along +x-dir.) and MRP = +30 ft ·lb
P
1'
1'
30 lb
40 lb
30 lb
•
x
y
Notes: Answer:
1. D

## Slide 37
ATTENTION QUIZ
2. Consider three couples acting on a body. Equivalent systems will be _______ at different points on the body.
A) different when located
B) the same even when located
C) zero when located
D) None of the above.
Notes: Answer:
2. B

## Slide 38
READING QUIZ
1. The resultant force (FR) due to a distributed load is equivalent to the _____ under the distributed loading curve, w = w(x).
A) centroid B) arc length
C) area D) volume
2. The line of action of the distributed load’s equivalent force passes through the ______ of the distributed load.
A) centroid B) mid-point
C) left edge D) right edge
x
w
F
R
Distributed load curve
Notes: Answers:
1. C
2. A

## Slide 39
APPLICATIONS
A distributed load on the beam exists due to the weight of the lumber.
Is it possible to reduce this force system to a single force that will have the same external effect? If yes, how?

## Slide 40
APPLICATIONS (continued)
The sandbags on the beam create a distributed load.
How can we determine a single equivalent resultant force and its location?

## Slide 41
DISTRIBUTED LOADING
In many situations a surface area of a body is subjected to a distributed load. Such forces are caused by winds, fluids, or the weight of items on the body’s surface.
We will analyze the most common case of a distributed pressure loading. This is a uniform load along one axis of a flat rectangular body.
In such cases, w is a function of x and has units of force per length.

## Slide 42
MAGNITUDE OF RESULTANT FORCE
Consider an element of length dx.
The force magnitude dF acting on it is given as
dF = w(x) dx
The net force on the beam is given by
+  FR = L dF = L w(x) dx = A
Here A is the area under the loading curve w(x).

## Slide 43
LOCATION OF THE RESULTANT FORCE
The force dF will produce a moment of (x)(dF) about point O.
The total moment about point O is given as
+ MRO = L x dF = L x w(x) dx
Assuming that FR acts at x, it will produce the moment about point O as
+ MRO = ( x ) (FR) = L x w(x) dx

## Slide 44
Comparing the last two equations, we get
LOCATION OF THE RESULTANT FORCE (continued)
You will learn later that FR acts through a point “C,” which is called the geometric center or centroid of the area under the loading curve w(x).

## Slide 45
EXAMPLES
Until you learn more about centroids, we will consider only rectangular and triangular loading diagrams whose centroids are well defined and shown on the inside back cover of your textbook.
In a rectangular loading, FR = 400  10 = 4,000 lb and x= 5 ft.
In a triangular loading ,
FR = (0.5) (6000) (6) = 1,800 N and x = 6 – (1/3) 6 = 4 m.
Note that the centroid in a right triangle is at a distance one third the width of the triangle as measured from its base.
x

## Slide 46
CONCEPT QUIZ
1. What is the location of FR, i.e., the distance d?
A) 2 m B) 3 m C) 4 m
D) 5 m E) 6 m
2. If F1 = 1 N, x1 = 1 m, F2 = 2 N and x2 = 2 m, what is the location of FR, i.e., the distance x.
A) 1 m B) 1.33 m C) 1.5 m
D) 1.67 m E) 2 m
F
R
x
F
2
F
1
x
1
x
2
F
R
B
A
d
B
A
3 m
3 m
Notes: Answers:
1. D
2. D

## Slide 47
GROUP PROBLEM SOLVING
Given: The loading on the beam as shown.
Find: The equivalent force and its location from point A.
Plan:
1) Consider the trapezoidal loading as two separate loads (one rectangular and one triangular).
2) Find FR and for each of these two distributed loads.
3) Determine the overall FR and for the three point loadings.
x

## Slide 48
GROUP PROBLEM SOLVING (continued)
For the combined loading of the three forces,
FR = 1.5 kN + 3 kN + 1.5 kN = 6 kN
+ MRA = (1.5) (1.5) + 3 (1) + (1.5) 4 = 11.25 kN • m
Now, FR = 11.25 kN • m Hence, = (11.25) / (6) = 1.88 m from A.
x
x
For the rectangular loading of height 0.5 kN/m and width 3 m,
FR1 = 0.5 kN/m  3 m = 1.5 kN
= 1.5 m from A
x
1
For the triangular loading of height 2 kN/m and width 3 m,
FR2 = (0.5) (2 kN/m) (3 m) = 3 kN
and its line of action is at = 1 m from A
x
2

## Slide 49
ATTENTION QUIZ
1. FR = ____________
A) 12 N B) 100 N
C) 600 N D) 1200 N
2. x = __________.
A) 3 m B) 4 m
C) 6 m D) 8 m
F
R
100 N/m
12 m
x
Notes: Answers:
1. C
2. B

## Slide 50
Find the equivalent resultant force and couple moment acting at A.
Find the magnitudes of the forces P and F and the distance d.