## Slide 1: Chapter 4
Moments
Sections 1 - 4

## Slide 2
What is the force on the lug nut?
How does it change if the hand moves to B?
This is a MOMENT
or
TORQUE

## Slide 3
Draw a FBD of the lug nut
Notes: Where does the lug nut feel the force? Probably along the circumference, maybe more on one side than the other. Simplify the forces into one place and draw a vector. Notice that the vector is on the edge of the body. This is why we switched from a particle model to a FBD. It’s important WHERE the force is drawn on the body because a moment causes rotation.

## Slide 4
MOMENT OF A FORCE
In the 2-D case, the magnitude of the moment is Mo = F d
As shown, d is the perpendicular distance from point O to the line of action of the force.
In 2-D, the direction of MO is either clockwise or
counter-clockwise depending on the tendency for rotation.

## Slide 5
MOMENT OF A FORCE
The moment of a force about a point provides a measure of the
tendency for rotation (sometimes called torque).

## Slide 6
Check
1. What is the moment of the 10 N force about point A (MA)?
A) 10 N·m B) 30 N·m C) 13 N·m
D) (10/3) N·m E) 7 N·m
A•
d = 3 m
F = 10 N
Notes: Answers:
1. B
2. A

## Slide 7
Notes: Figure: 04-04aEx1

## Slide 10
MOMENT OF A FORCE - SCALAR FORMULATION (continued)
For example, MO = F d and the direction is counter-clockwise.
Often it is easier to determine MO by using the components of F as shown.
Using this approach, MO = (FY a) – (FX b). Note the different signs on the terms! The typical sign convention for a moment in 2-D is that counter-clockwise is considered positive. We can determine the direction of rotation by imagining the body pinned at O and deciding which way the body would rotate because of the force.
F
a
b
d
O
a
b
O
F
F x
F y

## Slide 11
CONCEPT QUIZ
If a force of magnitude F can be applied in four different 2-D configurations (P,Q,R, & S), select the cases resulting in the maximum and minimum torque values on the nut. (Max, Min).
A) (Q, P) B) (R, S)
C) (P, R) D) (Q, S)
Notes: Answers:
1. D

## Slide 12
GROUP PROBLEM SOLVING
Find the moment of the force at O
Plan: 1) Resolve the force along x and y axes.
2) Determine MO using scalar analysis.
Solution: +  Fy = - 40 cos 20° N
+  Fx = - 40 sin 20° N
+ MO = {-(40 cos 20°)(200) + (40 sin 20°)(30)}N·mm
= -7107 N·mm = - 7.11 N·m

## Slide 13
Given: A 400 N force is applied to the frame and  = 20°.
Find: The moment of the force at A.
Plan:
1) Resolve the force along x and y axes.
2) Determine MA using scalar analysis.
EXAMPLE #1

## Slide 14
EXAMPLE #1 (continued)
Solution
+  Fy = -400 sin 20° N
+  Fx = -400 cos 20° N
+ MA = {(400 cos 20°)(2) + (400 sin 20°)(3)} N·m
= 1160 N·m

## Slide 16
MOMENT OF A FORCE – 3-D
Moments in 3-D can be calculated using scalar (2-D) approach but it can be difficult and time consuming. It is often easier to use the vector cross product.
Using the vector cross product, MO = r  F .
Here r is the position vector from point O to any point on the line of action of F.

## Slide 17
CROSS PRODUCT
In general, the cross product of two vectors A and B results in another vector C , i.e., C = A  B. The magnitude and direction of the resulting vector can be written as:
C = A  B = A B sin  UC
Here UC is the unit vector perpendicular to both A and B vectors as shown.

## Slide 18
CROSS PRODUCT
The cross product can be written as:
Each component can be determined using 2  2 determinants.
Expanding the 2  2 determinants we get
MO = (r y FZ - rZ Fy) i - (r x Fz - rz Fx ) j + (rx Fy - ry Fx ) k

## Slide 19
CROSS PRODUCT (continued)
The right hand rule is a useful tool for determining the direction of the resulting vector.
For example: i  j = k
Note that a vector crossed into itself is zero, e.g., i  i = 0

## Slide 22
Check
1. Moment of force F about point O is defined as MO = ___________ .
A) r x F B) F x r
C) r • F D) r * F
2. If M = r  F, then what will be the value of M • r ?
A) 0 B) 1
  C) r 2 F D) None of the above.
Notes: Answer: A, A

## Slide 23: 3. Another word for moment is __________
4. If you use Cartesian vectors to determine the moment of a force, you will use the ____________ (cross product / dot product)
Notes: Torque
Cross product

## Slide 26
EXAMPLE # 2
Given: a = 3 in, b = 6 in and c = 2 in.
Find: Moment of F about point O.
Plan:
1) Find rOA.
2) Determine MO = rOA  F .
Solution rOA = {3 i + 6 j – 0 k} in
i
j
k
3 6 0
3 2 -1
MO =
= [{6(-1) – 0(2)} i – {3(-1) – 0(3)} j + {3(2) – 6(3)} k] lb·in
= {-6 i + 3 j – 12 k} lb·in
o

## Slide 27
ATTENTION QUIZ
10 N
3 m P 2 m
5 N
1. Using the CCW direction as positive, the net moment of the two forces about point P is
A) 10 N ·m B) 20 N ·m C) - 20 N ·m
D) 40 N ·m E) - 40 N ·m
2. If r = { 5 j } m and F = { 10 k } N, the moment
r x F equals { _______ } N·m.
A) 50 i B) 50 j C) –50 i
D) – 50 j E) 0
Notes: Answers:
1. B
2. A